## Slide 1
Project Presentation of CO-OP Project at Industry (Module-2) (22CS421)
On
Adaptive OT Cybersecurity Solutions:
An Integrated Zero-Trust, Digital-Twin,
and Human-Centric Framework for Resilient ICS
Pratham Khatkar
2210991674 | B.E. Computer Science and Engineering
Supervised By
Dr. Gurpreet Singh (Mentor)
Department of Computer Science and Engineering,
Chitkara University, Punjab

## Slide 2
Agenda
1. Introduction
2. The AOCSF Framework
3. Pillar I: Zero-Trust Enforcement
4. Pillar II: Digital Twin Simulations
5. Pillar III: Human-Centric Training
6. Experimental Setup
7. Attack Detection Results
8. Latency & Operator Training Results
9. Ablation Analysis
10. Standards Compliance
11. Limitations & Future Work
12. Conclusion
2

## Slide 3
Introduction
The Problem
• Industry 4.0 dissolved the air-gap — IIoT, cloud & remote access exposed ICS to cyber threats • Legacy PLCs/RTUs have no authentication and cannot be patched • Perimeter-only defenses cannot detect physically dangerous but syntactically valid commands
Real-World Incidents
• Ukraine 2015 — SCADA attack cut power to 230,000 customers • Oldsmar 2021 — Water plant chemical manipulation attempt • Industroyer2 2022 — ICS protocol malware vs Ukrainian substations
Why Traditional Defenses Fail
• IT prioritises Confidentiality — OT prioritises Availability and Physical Safety • Microsecond control loop timing — VPN latency is operationally unacceptable
3

## Slide 4
The AOCSF Framework
Three pillars — each covers the blind spots of the others:
PILLAR I
Zero-Trust
Enforcement
• ABAC trust score formula
• Risk-stratified tiers (SC/PC/SV/TM)
• Edge-resident enforcement points
• PASG for legacy devices
PILLAR II
Digital Twin
Simulations
• Physics-aware command detection
• DRL Red/Blue co-evolution (200 eps)
• Sandboxed attack discovery
• Operator training sandbox
PILLAR III
Human-Centric
Training
• Behavioral fingerprinting
• Mahalanobis anomaly detection
• 6 DT scenario drill types
• After-action review system
4

## Slide 5
Pillar I: Zero-Trust Enforcement
Trust Score: T = w₁·Id(e) + w₂·Ps(t) + w₃·Bh(e,t) + w₄·Rc(r)
Id(e) = Identity 35% | Ps(t) = Process State 25% | Bh(e,t) = Behaviour 25% | Rc(r) = Resource 15%
Risk-Stratified Verification Tiers:
Risk Tier | Verification Frequency | AOCSF Latency
SC — Safety Critical | Every transmission | 8 ms
PC — Process Control | Every 250 ms | 6 ms
SV — Supervisory | Every 2 seconds | 3 ms
TM — Telemetry | Every 30 seconds | 1.5 ms
Key Points • Auth on edge-resident nodes — eliminates central server round-trip latency • Legacy devices: Protocol-Aware Security Gateways — no firmware changes needed • Result: 36.5 ms → 4.6 ms (87.3% reduction, Cohen's d=7.01, p<0.001)
5

## Slide 6
Pillar II: Digital Twin Simulations
IDS asks: "Does command look suspicious?" AOCSF asks: "Will command make reactor unsafe?"
1. Physics-Aware Anomaly Detection
• Every command simulated over look-ahead window L=10 steps • Alert fires if predicted trajectory exits safe operating bounds — regardless of protocol conformance • Catches FDI attacks completely invisible to network-layer IDS
2. DRL Red-Blue Co-evolution
• Red Agent autonomously discovers multi-step attack chains in sandboxed DT (Q-learning α=0.1, γ=0.95) • Blue Agent hardens detection from each discovery — 200 episodes, fully automated
3. Operator Training Sandbox
• 6 scenario types: FDI, MitM, Replay, Ransomware, Credential Spoofing, APT • Real HMI connected to process replica — realistic without risking live equipment
6

## Slide 7
Pillar III: Human-Centric Training
Behavioral Fingerprinting
• 5 features: keystroke timing, command n-grams, navigation patterns, action-context, shift timing • Baseline: 10 shifts | Alert threshold: Mahalanobis distance > θ = 3.0 SD • Detects credential spoofing even with a valid stolen password Training Results (n=15 operators, 18 drills over 3 weeks, paired t-test)
Metric | Before | After | Improvement
Incident ID Time | 314 s | 150 s | 52% faster (d=4.59, p<0.001)
Decision Accuracy | 69.3% | 90.5% | +21 pp (p<0.001)
Stress Error Rate | 15.9% | 4.4% | 72% lower (d=5.42, p<0.001)
All Cohen's d > 4.0 — large, practically significant effects confirmed.
7

## Slide 8
Experimental Setup
Testbed: Tennessee Eastman Process (TEP)
• Standard ICS benchmark — Downs & Vogel (1993) • 41 measured variables, 12 manipulated variables, 20 disturbances • Python, seed=42 (fully reproducible) | Cross-validated on SWaT dataset (36 attacks) • Baseline: VPN perimeter + standalone signature-based IDS
4 Controlled Experiments
• Exp 1 — Attack Detection: n=50 trials per attack type (4 attack vectors) • Exp 2 — Latency Benchmark: n=1,000 auth samples across 4 risk tiers • Exp 3 — Human Factor: n=15 operators, pre/post training, paired t-test • Exp 4 — DRL Co-evolution: 200 episodes, Red vs Blue agent learning
Statistics: α=0.05 | 95% Wilson confidence intervals | Cohen's d effect sizes
8

## Slide 9
Key Results: Attack Detection
Chart: 
| FDI | MitM | Replay | Cred. Spoofing
VPN+IDS Baseline | 14 | 34 | 16 | 28
AOCSF Framework | 96 | 82 | 100 | 100
Attack | Baseline | AOCSF
False Data Injection | 14% | 96%
Man-in-the-Middle | 34% | 82%
Replay Attacks | 16% | 100%
Credential Spoofing | 28% | 100%
Key Finding:
FDI attacks send syntactically valid commands — completely invisible to network IDS. Only the physics-aware Digital Twin detects them by simulating physical consequences.
SWaT cross-validation: 89.3% detection vs 71.2% IDS baseline
9

## Slide 10
Key Results: Latency & Operator Training
Authentication Latency by Risk Tier
Chart: 
| SC | PC | SV | TM
VPN Baseline | 41.9 | 38.2 | 34.5 | 31.5
AOCSF | 8 | 6 | 3 | 1.5
87.3% reduction: 36.5ms → 4.6ms (d=7.01, p<0.001)
Operator Performance Pre vs Post Training
Chart: 
| ID Time(s÷10) | Accuracy(%) | Error(%)
Pre-Training | 31.4 | 69.3 | 15.9
Post-Training | 15 | 90.5 | 4.4
52% faster ID | +21pp accuracy | 72% fewer errors
n=15 operators | All p<0.001 | Cohen's d > 4.0
96%
FDI Detected
87%
Latency Cut
52%
Faster ID
72%
Errors Down
10

## Slide 11
Ablation Analysis: Why All 3 Pillars Are Needed
Remove any one pillar — comprehensive coverage collapses
Attack Type | ZT Only | DT Only | HC Only | All 3 Together
False Data Injection | ❌ 0% | ✅ 96% | ❌ 0% | ✅ 96%
Man-in-the-Middle | ✅ 72% | ⚠ 45% | ⚠ 32% | ✅ 82%
Replay Attacks | ✅ 100% | ⚠ 40% | ⚠ 20% | ✅ 100%
Credential Spoofing | ⚠ 28% | ❌ 12% | ✅ 84% | ✅ 100%
Conclusion: ZT has no physics model → misses FDI. DT alone misses credential spoofing. HC alone misses FDI. Only the integrated three-pillar design achieves comprehensive coverage across all attack vectors.
11

## Slide 12
Standards Compliance
IEC 62443 — Security Levels 2 and 3
• FR 1 (Identity & Authentication) — ABAC continuous verification at SL-2/3 • FR 2 (Use Control) — Least-privilege, trust-score gating
• FR 3 (System Integrity) — DT physics-aware anomaly detection at SL-3
• FR 6 (Incident Response) — Behavioral telemetry as automatic compliance evidence
NIST SP 800-82 Rev.3 + SP 800-207
• SP 800-82: Continuous monitoring, defense-in-depth for OT environments • SP 800-207: All 5 ZTA design principles, adapted for OT latency constraints
Practical Advantage: Compliance evidence generated automatically — telemetry logs, access records & DT anomaly reports satisfy IEC 62443 documentation needs with zero separate overhead.
12

## Slide 13
Limitations & Future Work
Limitations 1. Simulation only — TEP & SWaT benchmarks, not live industrial plants 2. n=15 operators — adequate for large effects, not full generalizability 3. Edge hardware: min 4-core CPU, 8 GB RAM required 4. Behavioral monitoring needs workforce privacy governance policy
Future Directions
1. Live pilot deployment via Rockwell Automation partnership 2. Automated digital twin generation tooling 3. Privacy-preserving federated behavioral telemetry 4. Formal IEC 62443 SL-2/3 certification 5. Multi-plant distributed DRL attack scenarios
13

## Slide 14
Conclusion
Key Findings
• 96% FDI detection — structurally invisible to network IDS, caught by physics-aware DT
• 87.3% latency reduction: 36.5ms → 4.6ms (Cohen's d=7.01, p<0.001)
• 52% faster incident ID: 314s → 150s (d=4.59, p<0.001)
• Ablation confirms: all 3 pillars necessary — no single pillar achieves full coverage Takeaway
OT security at the IT/OT boundary requires simultaneous treatment of access control, physics-aware detection, and human factors. The integrated design produces synergies no single-pillar system can replicate.
The simulation results are a starting point. What this framework needs next is to be tested somewhere that has real stakes.
14

## Slide 15
Thank You
Questions & Discussion
Pratham Khatkar | pratham674.be22@chitkara.edu.in
Department of Computer Science and Engineering, Chitkara University, Punjab
15